## Slide 1: Wireless Connection

## Slide 2: Outcomes
To experiment with wireless connectivity for microcontrollers.
  Setting up the IDE for a wireless uC.
  Connecting to the WiFi.
  Accessing the internet.

## Slide 3: ESP32 & ESP8266
Low cost microcontrollers with built in WiFi and TCP/IP. (Espressif Systems, China, 2014)
Extremely popular for wireless projects.
ESP8266 is earlier implementation.
ESP32 is the successor to ESP8266. More powerful microcontroller. Usually includes Bluetooth.

## Slide 4
As of May 2025. ESP8266 boards are generally cheaper!

## Slide 6: Bells & Whistles!
ESP devices are a little bit bare bones. Some of the nice features we are used to are not implemented easily.
This can depend on the platform/form factor of the device, eg: analogue input/outputs
Logic levels will be different too – typically 3.3 volts!
  Check requirements on sensors
  You might need to use a bi-directional logic level converter

## Slide 8: Digital IO
The PinMode() method works on the GPIO pin number for esp32 and esp8266.
  GPIO5?
  PinMode(5, INPUT)
Remember pull up and pull down resistors. Some devices do allow:
  (PinMode pin_no, INPUT_PULLUP)

## Slide 9: Analogue IO
Depends very much on the board layout you are using!
Some board will have dedicated Analogue pins
Pulse Width Modulation can be used for analogue output.

## Slide 10: Other Features
I2C
Interupts
Most Arduino C software features will be supported if the device is supported by the IDE.

## Slide 11: Setting up the IDE.
ESP devices are not Atmel devices (The default uC for Arduino platform)
We usually have to:
  Update the URL for additional boards in Preferences
  Use the Boards Manager to change our default board.

## Slide 14: Connecting to WiFi
We have a router in D312 we can use to experiment with:
SSID - D_Block_Lab
Pass - P@ssw0rd

## Slide 15: Accessing the Internet.
We have a couple of supplied Sketches for connecting your device to the wifi.
Can you retrieve the contents of a webpage with it?
You will need to do some digging around!
Try and access:
info.cern.ch